## Slide 1: Network Models

## Slide 2: Network Models
Topology describes how parts of a whole work together
Physical topology mostly refers to a network’s hardware and how computers, other devices, and cables work together to form the physical network
Logical topology refers to how software controls access to network resources
  It includes how users and software initially gain access to the network
A network operating system (NOS) controls access to the entire network
  A NOS is required by client-server models

## Slide 3: Peer-to-Peer Network Model (1 of 2)
In a peer-to-peer (P2P) network model the OS of each computer on the network is responsible for controlling access to its resources
  There is no centralised control
Computers, called nodes or hosts, form a logical group of computers and users
  Each computer controls its own administration, resources, and security
Advantages
  Simple configuration
  Less expensive compared to other network models
Disadvantages
  Not scalable
  Not necessarily secure
  Not practical for large installations

## Slide 4: Peer-to-Peer Network Model (2 of 2)
Figure 1-1 In a peer-to-peer network, no computer has more authority than another; each computer controls its own resources and communicates directly with other computers​

## Slide 5: Client-Server Network Model (1 of 3)
Resources are managed by the NOS via a centralised directory database
A Windows domain is a logical group of computers that a Windows Server can control

## Slide 6: Client-Server Network Model (1 of 3)
Active Directory (AD) is the centralised directory database that contains user account information and security for the entire group of computers
A user can sign on to the network from any computer on the network and gain access to the resources that AD allows
  This process is managed by Active Directory Domain Services (AD DS)
A computer making a request from another is called the client

## Slide 7: Client-Server Network Model (2 of 3)
Figure 1-2 A Windows domain uses the client-server model to control access to the network, where security on each computer or device is controlled by a centralised database on a domain controller

## Slide 8: Client-Server Network Model (3 of 3)
The NOS is responsible for:
  Managing client data and other resources
  Ensuring authorised user access
  Controlling user file access
  Restricting user network access
  Dictating computer communication rules
  Supplying applications and data files to clients
Servers that have a NOS installed require:
  More memory, processing power, and storage capacity
  Equipped with special hardware to provide network management functions

## Slide 9: Client-Server Applications (1 of 2)
Network services are the resources a network makes available to its users
  It includes applications and the data provided by these applications
In client-server applications:
  A client computer requests data or a service from a second computer, called the server

## Slide 10: Client-Server Applications (2 of 2)
Figure 1-3 A web browser (client application) requests a web page from a web server (server application); the web server returns the requested data to the client

## Slide 11: Network Services and Their Protocols (1 of 2)
Protocols are methods and rules for communication between networked devices
Two primary network protocols:
  TCP (Transmission Control Protocol)
  IP (Internet Protocol)
Popular client-server applications include:
  Web service
  Email services
  DNS service
  FTP service
  Database services
  Remote access service

## Slide 12: Network Services and Their Protocols (2 of 2)
Figure 1-5 SMTP is used to send email to a recipient’s email server, and POP3 or IMAP4 is used by the client to receive email