## Slide 1: Infrastructure

## Slide 2: Components of Structured Cabling
ANSI/TIA-568 Commercial Building Wiring Standard
  Also known as structured cabling
The wiring standard describes the best way to install networking media to maximise performance and minimise upkeep
  The principles apply no matter what type of media, transmission technology, or networking speeds are involved
Structured cabling is based on a hierarchical design and assumes a network is based on the star topology

## Slide 3: From the Demarc to a Workstation (1 of 11)

## Slide 4: From the Demarc to a Workstation (2 of 11)
Entrance Facility in Building A:
  EF (entrance facility) – location where the incoming network (such as Internet) connects with the school or corporate network
  Demarc (demarcation point) – the device that marks where a telecommunications service provider’s network ends and the organisation’s network begins

## Slide 5: From the Demarc to a Workstation (2 of 11)
Entrance Facility in Building A:
  MDF (main distribution frame) – the centralised point of interconnection for an organisation’s LAN or WAN (also called MC or main cross connect)
  Data room – an enclosed space that hold network equipment (also called data closet, data centre, equipment room, or telecommunications room)
  Rack – holds various network equipment
  Patch panel – a panel of data receptors which can be mounted to a wall or a rack
    A patch panel provides a central termination point when many patch cables converge in a single location

## Slide 6: From the Demarc to a Workstation (3 of 11)

## Slide 7: From the Demarc to a Workstation (4 of 11)

## Slide 8: From the Demarc to a Workstation (5 of 11)

## Slide 9: From the Demarc to a Workstation (6 of 11)
Entrance Facility in Building A (continued):
  VoIP telephone equipment – VoIP (Voice over IP) is the use of any network to carry voice signals using TCP/IP protocols
  In one or more data rooms you might find the following:
    VoIP gateway
    VoIP PBX
    VoIP endpoints

## Slide 10: From the Demarc to a Workstation (6 of 11)
Data Room in Building B:
  IDF (intermediate distribution frame) – provides an intermediate connection between the MDF and end-user equipment on each floor and in each building
Work Areas in All Three Buildings:
  Work area – encompasses workstations, printers, and other network devices
  Wall jacks – the ANSI/TIA standard calls for each wall jack to contain at least one voice and one data outlet

## Slide 11: From the Demarc to a Workstation (7 of 11)

## Slide 12: From the Demarc to a Workstation (8 of 11)

## Slide 13: From the Demarc to a Workstation (9 of 11)
Rack Systems
  Racks come in two-post and four-post varieties (though six-post racks are also available)
  Racks may be wall- or ceiling-mounted, freestanding on the floor, or bolted to the floor
  Consider the following when purchasing racks:
    Height – rack height is measured in rack units (RU or U) with the industry standard being 42U tall
    Width – equipment racks come in a standard 19-inch frame (19 inches wide)
    Depth – rack depths vary between manufacturers
  In data centres containing multiple rows of racks, a hot aisle/cold aisle layout pulls cool air from vents in the floor or from low-lying wall vents into rows of racks (see Figure 2-14)

## Slide 14: From the Demarc to a Workstation (10 of 11)

## Slide 15: From the Demarc to a Workstation (11 of 11)