## Slide 1: Cabling

## Slide 2: Cabling (1 of 5)
Types of Cables
  Patch cable – a relatively short length of cabling with connectors at both ends
  Horizontal cabling – connects workstations to the closest data room and to switches housed in the room
  Backbone cabling – consists of cables or wireless links that provide interconnection between the entrance facility and MDF and between MDF and IDFs
  Many network problems are the result of poor cable installations
    Pay close attention to the quality of cable connections and cable management

## Slide 3: Cabling (2 of 5)

## Slide 4: Cabling (3 of 5)

## Slide 5: Cabling (4 of 5)
Cable Management
  Termination – when terminating twisted-pair cabling, don’t leave more than 1 inch of exposed cable before a termination
  Bend radius – do not exceed the cable’s prescribed bend radius, which is the radius of the maximum arc into which you can loop a cable without impairing data transmission
  Continuity – use a cable tester to verify that each cable segment transmits data reliably
  Loosely cinch cables

## Slide 6: Cabling (4 of 5)
Cable Management
  Cable coverings and conduits – avoid laying cables across a floor and use cord covers if they must be exposed
  EMI sources – install cable at least 3 feet away from fluorescent lights or other sources of EMI (electromagnetic interference)
  Plenum cabling – if running cable in the plenum (the area above the ceiling tile or below subflooring), make sure the cable sheath is plenum-rated

## Slide 7: Cabling (5 of 5)
Cable Management (continued)
  Grounding - pay attention to grounding requirements
  Slack in cable runs
  Cable trays - use cable management devices such as cable trays, braided sleeving, and furniture grommets
  Patch panels - use patch panels to organise and connect lines
  Company standards and inventory
  Documentation
    Keep your cable plant documentation accessible
    Label every data jack or port, patch panel and connector
    Use color-coded cables for different purposes
    Update your documentation as you make changes to the network