## Slide 1: Addressing issues

## Slide 2: Troubleshooting Address Problems

## Slide 3: Troubleshooting Tools (1 of 8)
Command-line tools are a great resource to troubleshoot network problems
ping (Packet Internet Groper) utility is used to verify that TCP/IP is:
  Installed
  Bound to the NIC
  Configured correctly
  Communicating with the network
The ping utility sends out a signal called an echo request to another device (request for a response)
  The other computer responds in the form of an echo reply
ICMP (Internet Control Message Protocol) is the protocol used by the echo request/reply to carry error messages and information about the network

## Slide 4: Troubleshooting Tools (2 of 8)
IPv6 networks use a version of ICMP called ICMPv6
  ping6 – on Linux computers running IPv6, use ping6 to verify whether an IPv6 host is available
  ping -6 – on Windows computers, use ping with the -6 switch to verify connectivity on IPv6 networks
For the ping6 and ping -6 commands to work over the Internet, you must have access to the IPv6 Internet

## Slide 5: Troubleshooting Tools (3 of 8)
The ipconfig command shows current TCP/IP addressing and domain name information on a Windows computer
  Use ipconfig/all to see a more complete summary of TCP/IP addressing information

## Slide 6: Troubleshooting Tools (4 of 8)

## Slide 7: Troubleshooting Tools (5 of 8)
Use the ip utility to view and manage TCP/IP settings
The ip utility is only available on UNIX and Linux systems
Any ip commands that change the state of a link require elevated privileges
  This is accomplished by logging in as the root user or by temporarily elevating the current user's privileges with the sudo (superuser do) command
ifconfig is a similar utility used to view and manage TCP/IP settings
If your Linux or UNIX system provides a GUI
  Open a shell prompt, then type ifconfig

## Slide 8: Troubleshooting Tools (6 of 8)

## Slide 9: Troubleshooting Tools (7 of 8)
The nslookup (name space lookup) utility allows you to query the DNS database from any computer on a network
  To find the host name of a device by specifying its IP address, or vice versa
  It is useful for verifying a host is configured correctly or for troubleshooting DNS resolution problems
Reverse DNS lookup - to find the host name of a device whose IP address you know
  nslookup 69.23.208.74

## Slide 10: Troubleshooting Tools (7 of 8)
The nslookup utility is available in two modes:
  Interactive - to test multiple DNS servers at one time
  Noninteractive - test a single DNS server
You can change DNS servers from within interactive mode with the server subcommand and specifying the IP address of the new DNS server
To exit nslookup’s interactive mode, enter exit

## Slide 11: Troubleshooting Tools (8 of 8)
The dig (domain information groper) utility is available on Linux and macOS
  Provides more detailed information than nslookup and uses more reliable sources of information to output its results
Use dig to query DNS nameservers for information about host addresses and other DNS records
An IP scanner can be used to gather information about all devices connected to a network

## Slide 12: Common Network Issues (1 of 2)
Incorrect time
  Check a domain computer’s time source from a Command Prompt window by entering w32tm /query /source
DHCP Issues
  If you are getting DHCP errors or if multiple clients are having trouble connecting to the network, try the following:
    Check the settings on your DHCP server
    Make sure the DHCP scope is large enough to account for the number of clients the network must support
  Consider implementing a shorter lease time on larger networks

## Slide 13: Common Network Issues (2 of 2)
Network Connection Configuration Issues
  Common configuration errors:
    Incorrect IP address
    Duplicate IP address
    Incorrect subnet mask
    Incorrect gateway
    Incorrect DNS or DNS issues
  When a computer is struggling to establish a network connection
    Check its TCP/IP configuration settings
  If the computer is not obtaining an IP address and related information from a DHCP server
    Static settings might be using the wrong information
    Try switching to DHCP