## Slide 1: Routing I

## Slide 2: Routers and How They Work
A router joins two or more networks and passes packets from one network to another
Routers can do the following:
  Connect dissimilar networks (LANs and WANs)
  Interpret Layer 3 and often Layer 4 addressing
  Determine the best path for data to follow from point A to point B
  Reroute traffic if the path of first choice is down but another path is available

## Slide 3: Routers and How They Work

## Slide 4: Routers and How They Work
Routers may perform any of the following optional functions:
  Filter broadcast transmissions
  Prevent certain types of traffic from getting to a network
  Support simultaneous local and remote connectivity
  Provide high network fault tolerance through redundant components such as power supplies
  Monitor network traffic and report statistics
  Diagnose internal or other connectivity problems and trigger alarms

## Slide 5: Routers and How They Work
Router categories:
  Core routers, also called interior routers—Direct data between networks within the same autonomous system (A S)
  Edge routers, or border routers—Connect an autonomous system with an outside network
  Exterior routers—Refers to any router outside the organisation’s A S
    Direct data between autonomous systems

## Slide 6: Autonomous Systems
An Autonomous System is a collection of networks under a common administration (a single organisation, ISP or systems administrator) and sharing a common routing strategy.
Typically the world wide organisation ICANN, the ISP, or the administrator assigns a unique AS number to the Autonomous System.
The Autonomous System number uniquely distinguish it from other Autonomous Systems around the world.
Each Autonomous Systems has its own set of rules and policies.

## Slide 8: Multilayer Switches
Layer 3 switch—Capable of interpreting Layer 3 data and works much like a router:
  Usually faster and less expensive
  Primary difference is the way the hardware is built
Layer 4 switch—Capable of interpreting Layer 4 data:
  Also known as content or application switches
  Enables switch to perform advanced filtering, keep statistics, and provide security functions
  Typically used as part of a network’s backbone

## Slide 9: Routing Tables
Routing table—A database that maintains information about where hosts are located and the most efficient way to reach them
  Routers rely on them to identify which router is the next hop to reach a particular destination host
Routing tables contain IP addresses and network masks that identify a network that a host or another router belongs to

## Slide 10: Routing Tables

## Slide 11: Routing Path Types
Static routing—Network administrators configures a routing table to direct messages along specific paths
  Example—A static route between a small business and its I S P
Dynamic routing—Automatically calculates the best path between two networks and maintains this information in a routing table
  Router can detect problems with failed or congested routes and reroute messages through a different path

## Slide 12: The route Command
The route command allows you to view a host’s routing table:
  On a Linux or UNIX system, use the command route
  On a Windows-based system, use the command route print
  On a Cisco I O S, use the command show ip route

## Slide 13: Routing Metrics
Routing metrics—Properties of a route used by routers to determine the best path to a destination:
  Hop count
  Theoretical bandwidth and actual throughput
  Delay, or latency, on a potential path
  Load, or the traffic or processing burden
  M T U (maximum transmission unit) or the largest I P packet size in bytes allowable without fragmentation
  Routing cost, or a value assigned to a particular route
  Reliability of a potential path
  Topology of a network