## Slide 1: Routing II

## Slide 2: Routing Protocols to Determine Best Paths
Routing protocols—Used by routers to communicate with each other to determine the best path
Routers rate the reliability and priority of a routing protocol’s data based on these criteria:
  Administrative distance (A D)—A number indicating the protocol’s reliability
  Convergence time—Time it takes to recognise a best path in the event of a change or network outage
  Overhead—The burden placed on the underlying network to support the protocol

## Slide 3: Routing Protocols to Determine Best Paths
Routing Protocol | Type | Algorithm Used
R I P (Routing Information Protocol) | I G P | Distance-vector
R I Pv2 (Routing Information Protocol, version 2) | I G P | Distance-vector
O S P F (Open Shortest Path First) | I G P | Link-state
I S-I S (Intermediate System to Intermediate System) | I G P | Link-state
E I G R P (Enhanced Interior Gateway Routing Protocol) | I G P | Advanced distance-vector
B G P (Border Gateway Protocol) | E G P | Advanced distance-vector or path vector

## Slide 4: Interior and Exterior Gateway Protocols
I G P (interior gateway protocols)—Used by core routers and edge routers within autonomous systems and are often grouped according to the algorithms they use to calculate best paths:
  Distance-vector routing protocols—Calculate path on the basis of the distance to that destination
  Link-state routing protocols—Enables routers to communicate beyond neighbouring routers in order to independently map the network and determine the best path

## Slide 5: Interior and Exterior Gateway Protocols
E G P (exterior gateway protocols)—Used by edge routers and exterior routers to distribute data outside of autonomous systems
  The only E G P currently in use is B G P

## Slide 6: Interior and Exterior Gateway Protocols

## Slide 7: Interior and Exterior Gateway Protocols
O S P F (Open Shortest Path First)—An I G P and a link-state protocol used on interior or border routers
  Introduced as an improvement to R I P
  Characteristics:
    Supports large networks—Imposes no hop limits (unlike R I P)
    Uses a more complex algorithm for determining best paths
    Shared data—Maintains a database of other routers’ links
    Low overhead, fast convergence—Demands more memory and C P U power for calculations, but keeps network bandwidth to a minimum and provides a very fast convergence time
    Stability—Uses algorithms that prevent routing loops
    Multi-vendor routers—Supported by all modern routers

## Slide 8: Interior and Exterior Gateway Protocols
I S-I S (Intermediate System to Intermediate System)—An I G P and link-state routing protocol:
  Uses a best-path algorithm similar to O S P F
  Is designed for use on core routers only (unlike O S P F)
  Not handcuffed to I P v 4 (like O S P F) so it’s easy to adapt to I P v 6
  Service providers generally prefer I S-I S because it’s more scalable than O S P F

## Slide 9: Interior and Exterior Gateway Protocols
E I G R P (Enhanced Interior Gateway Routing Protocol)—An advanced distance-vector protocol that combines some of the features of a link-state protocol
  Often referred to as a hybrid protocol
  Fast convergence time and low network overhead
  Easier to configure and less C P U-intensive than O S P F
  Supports multiple protocols and limits unnecessary network traffic between routers
  Originally proprietary to Cisco routers

## Slide 10: Interior and Exterior Gateway Protocols
B G P (Border Gateway Protocol)—The only current E G P and is known as the “protocol of the Internet”
  Can span multiple autonomous systems
  A path-vector routing protocol that communicates via B G P-specific messages that travel between routers
  Determines the best paths based on many different factors
  Can be configured to follow policies that might avoid a certain router or instruct a group of routers to prefer a particular route
  The most complex of the routing protocols

## Slide 11: ARP Tables and Routing Tables

## Slide 12: Routing – Role of Layer 2 and Layer 3 Addressing
Remember: Regardless of the routing protocol, packets travel across each individual link in a new frame of the appropriate format for the protocol running over that link.
1. From Host A to the router FastEthernet interface: Ethernet frame
2. Over the serial link on the left router to the right router: HDLC frame
3. From the router FastEthernet interface to Host D: Ethernet frame

## Slide 13: Forwarding an IP Packet
When a frame is received at a router interface.
The MAC address is checked to see if the frame is either addressed to the router interface or is a broadcast
The frame header and trailer are removed, and the packet is passed up to Layer 3
The routing table is examined to check for a match with the destination IP address of the packet
A match will identify the IP address of the directly connected next hop interface.
The next hop IP is only used to look up the MAC address of the next hop interface in the ARP table to construct a frame
The packet is placed into the new frame with the MAC address of the next hop interface as the destination address
The frame is queued on the appropriate outgoing interface until it is transmitted