## Slide 1: VLANs

## Slide 2: VLAN Trunks (1 of 2)
Each port on a switch that supports VLANs is configured as one of two types of VLAN ports:
  Access port – connects the switch to a host
  Trunk port – connects the switch to a networking device such as a router or another switch and manages traffic from multiple VLANs

## Slide 3: VLAN Trunks (1 of 2)
A trunk is a single physical connection between switches through which many logical VLANs can transmit and receive data
Trunking protocols assign and interpret VLAN tags in Ethernet frames
Cisco’s VTP (VLAN trunking protocol) is the most popular protocol for exchanging VLAN information over trunks
  VTP allows changes to a VLAN database on one switch, called the stack master, to be communicated to all other switches in the network

## Slide 4: VLAN Trunks (2 of 2)

## Slide 5: VLANs and Subnets (1 of 3)
In most situations, each VLAN is assigned its own subnet of IP addresses
The sample network in Figure 8-27, on the following slide, is divided into subnets
  The router sees three logical LANs connected to a single router port

## Slide 6: VLANs and Subnets (2 of 3)

## Slide 7: VLANs and Subnets (3 of 3)

## Slide 8: Types of VLAN (1 of 2)
Common VLAN types include the following:
  Default VLAN – typically preconfigured on a switch and initially includes all switch ports
  Native VLAN – receives all untagged frames from untagged ports
  Data VLAN – carries user-generated traffic, such as email, web browsing, or database updates
  Management VLAN – can be used to provide administrative access to a switch
  Voice VLAN – supports VoIP traffic
  Private VLAN – partitions a VLAN broadcast domain into subdomains
    Two types of secondary VLANs are:
      Isolated VLAN
      Community VLAN

## Slide 9: Types of VLAN (2 of 2)

## Slide 10: View Configured VLANs (1 of 2)
Once you create a VLAN, you maintain it via switch software
Figure 8-30 illustrates the output of a show vlan command on a Cisco switch
  This command is used to list the current VLAN recognized by a switch

## Slide 11: View Configured VLANs (2 of 2)
Figure 8-30 Output of the show vlan command on a Cisco switch

## Slide 12: Dynamic VLAN Assignment
A device might receive a dynamic VLAN assignment according to the following:
  Client device information, such as MAC address or location
  Authentication processes in cooperation with a RADIUS server can be used to distinguish which traffic should be assigned to which VLANs
  Devices that have not yet authenticated to the network or who authentication failed can be placed in a quarantine VLAN
  All WLAN traffic might be grouped within the same VLAN

## Slide 13: Troubleshoot and Secure VLANs (1 of 2)
Common configuration errors include the following:
  Incorrect VLAN assignment – can happen due to a variety of situations
  Incorrect port mode – switch ports connected to endpoints should nearly always use access mode
  VLAN isolation – you can potentially cut off an entire group from the rest of the network
VLAN hopping occurs when an attacker generates transmissions that appear to belong to a protected VLAN
  The attacker then crosses VLANs to access sensitive data or inject harmful software
There are two approaches to VLAN hopping:
  Double tagging
  Switch spoofing

## Slide 14: Troubleshoot and Secure VLANs (2 of 2)
Mitigation efforts to reduce the risk of VLAN hopping include the following:
  Don’t use the default VLAN
  Change the native VLAN to an unused VLAN ID
  Disable auto-trunking on switches that don’t need to support traffic from multiple VLANs
  On switches that carry traffic from multiple VLANs, configure all ports as access ports unless they are used as trunk ports
  Specify which VLANs are supported on each trunk instead of accepting a range of all VLANs
  Use physical security methods such as door locks to restrict access to network equipment