## Slide 1: CP1402 – Internet Fundamentals
VLSM
Variable-Length Subnet Masks

## Slide 2: Supernetting
Supernetting
  Combine contiguous networks that all use the same CIDR block into one supernet
  Also called classless routing or IP address segmentation
Supernetting is helpful for two reasons:
  Reduce the number of routing table entries by combining several entries
  Allow a company to create a single network made up of more than one Class C license

## Slide 3: Supernetting
Supernet: 192.168.88.0/22
Notes: Supernetting

## Slide 4: Example
  Let’s calculate the supernet for
    209.224.18.0/24
    209.224.21.0/24
    209.224.22.0/24
Dissimilar Octet | Convert to binary | Determine common bits | 
18 | 00010010 | 00010 | 010
21 | 00010101 | 00010 | 101
22 | 00010110 | 00010 | 110
Supernet octet is: |  | 16 | 
  The first two octets are the same, so 16 bits initially in common.
  5 bits in common: so mask is 16 + 5 = 21
  Supernet: 209.224.16.0/21

## Slide 5: POGIL 4 - Supernetting
  What is the single summarised network address and mask for
    201.10.177.0/24
    201.10.181.0/24
    201.10.184.0/24
    201.10.188.0/24