## Slide 1: WLAN Standards

## Slide 2: 802.11 WLAN Standards
WLANs work at OSI Layers 1 and 2
  They support TCP/IP higher-layer OSI protocols and operating systems
Most popular standards used by WLANs is referred to as Wi-Fi (wireless fidelity)
Notable Wi-Fi standards
  802.11b, 802.11a, 802.11g, 802.11n, 802.11ac, and 802.11ax
  802.11n and later modify the way frames are used at the MAC sublayer (lower portion of the Data Link layer)
  The LLC sublayer is primarily concerned with multiplexing, flow and error control, and reliability

## Slide 3: 802.11 Innovations (1 of 3)
Several innovations have been implemented that contribute to making later 802.11 standards much faster and much more reliable:
  Channel bonding – two adjacent 20-MHz channels can be bonded to make 40-MHz channel
    It more than doubles the bandwidth available in single 20-MHz channel

## Slide 4: 802.11 Innovations (1 of 3)
  MIMO (multiple input-multiple output) – multiple access point and client device antennas may issue signal to one or more receivers
    MIMO increases range and a network’s throughput
  MU-MIMO (multiuser MIMO) – a newer technology that allows multiple antennas to service multiple clients simultaneously
    MU-MIMO reduces congestion and contributes to faster data transmission
    MU-MIMO is available with WAVE 2 802.11ac products

## Slide 5: 802.11 Innovations (2 of 3)
Several innovations have been implemented that contribute to making later 802.11 standards much faster and much more reliable (continued):
  OFDMA (Orthogonal Frequency Division Multiple Access) – supports more efficient multiuser functionality for 80211 ax devices
  Frame aggregation combines multiple frames into one larger frame
    Networks can use one of two techniques for combining multiple data frames:
      A-MSDU (Aggregated Mac Service Data Unit)
      A-MPDU (Aggregated Mac Protocol Data Unit)

## Slide 6: 802.11 Innovations (3 of 3)

## Slide 7: Access Method (1 of 2)
802.11 MAC services append 48-bit physical addresses to frame to identify source and destination
The use of the same physical addressing scheme as other Ethernet networks allows easy combination with other IEEE networks
Wireless devices are not designed to simultaneously transmit and receive

## Slide 8: Access Method (1 of 2)
802.11 standards specify the use of CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance) procedures to access a shared medium
  Uses ACK packets to verify every transmission and requires more overhead than 802.3
RTS/CTS (Request to Send/Clear to Send) protocol ensures packets are not inhibited by other transmissions
  RTS/CTS decreases network efficiency, but can be efficient for large transmission packets

## Slide 9: Access Method (2 of 2)

## Slide 10: Association and Wireless Topologies (1 of 3)
Association is the process where packets are exchanged between computer and an access point in order to gain Internet access
Scanning occurs when a wireless devices surveys its surroundings for an access point
  In active scanning the wireless client takes the initiative by transmitting a special frame known as a probe
  In passive scanning the AP takes the initiative
    The wireless devices listens for special signal known as a beacon fame

## Slide 11: Association and Wireless Topologies (1 of 3)
SSID (service set identifier) is a unique character string identifying an access point
  The SSID is contained in the beacon frame information
  The SSID is configured in the AP’s configuration utility, and it is recommended that it be changed from the default setting

## Slide 12: Association and Wireless Topologies (2 of 3)
IEEE terms that reflect the most common wireless topologies include the following:
IBSS (Independent basic service set) using an ad hoc topology – a small number of nodes closely positioned transmit directly to each other without an intervening connectivity device
BSS (basic service set) using an infrastructure topology – a group of stations share an access point
  The identifier for this group of nodes is known as a BSSID (basic service set identifier)

## Slide 13: Association and Wireless Topologies (2 of 3)
ESS (extended service set) using a mesh topology – several access points are connected to same LAN network
  These APs are configured and managed by a wireless LAN controller
  Clients that belong to the same ESS share a special identifier called an ESSID (extended service set identifier)
  The ESSID allows a user to roam, or change from AP to AP

## Slide 14: Association and Wireless Topologies (3 of 3)

## Slide 15: IEEE 802.11 Frames (1 of 2)
802.11 specifies a MAC sublayer frame type
These frame types are divided into three groups:
  Management frames – association and reassociation
  Control frames – medium access and data delivery
    Examples of control frames include ACK and RTS/CTS frames
  Data frames – carry data sent between stations

## Slide 16: IEEE 802.11 Frames (2 of 2)