## Slide 1: Wi-Fi Security

## Slide 2: Wi-Fi Network Security
By default, the 802.11 standard offers no security
Authentication – allows a client to log on to the network either by providing the correct password for the SSID or by providing user credentials processed by an authentication server
  MAC filtering prevents the AP from authenticating any device whose MAC address is not listed
Encryption algorithms – scramble data into a format that cannot easily be interpreted if the signal is intercepted

## Slide 3: WPA (Wi-Fi Protected Access)
WPA (Wi-Fi Protected Access) dynamically assigns every transmission its own key
802.11i incorporates an encryption key generation and management scheme known as TKIP (Temporal Key Integrity Protocol) to improve security for legacy WEP-based devices
TKIP accomplished the following improvements:
  Message integrity
  Key distribution
  Encryption

## Slide 4: WPA2 (Wi-Fi Protected Access, Version 2)
WPA2 uses stronger data confidentiality methods
CCMP, which is short for Counter Mode with CBC (Cipher Block Chaining) MAC (Message Authentication Code) Protocol, helps ensure data confidentiality with both encryption and packet authentication by providing the following:
  Message integrity – ensures incoming packets are coming from their declared source
  Encryption – uses AES (Advanced Encryption Standard), which provides faster and more secure encryption than TKIP

## Slide 5: Personal and Enterprise (1 of 2)
The most secure communication is made possible by combining a RADIUS server with WPA/WPA2
  Known as WPA-Enterprise or WPA2-Enterprise
RADIUS (Remote Authentication Dial-in User Service) is an open-source authentication and authorisation service
  A RADIUS server is used in cooperation with an authentication mechanism called EAP
EAP (Extensible Authentication Protocol) provides the framework for authenticating clients and servers
EAP functions alongside RADIUS by organising communications with the network client devices, while RADIUS handles the actual authentication on the server

## Slide 6: Personal and Enterprise (2 of 2)

## Slide 7: Other Security Configurations
Additional security options include the following:
  AP and antenna placement
  Geofencing
  Guest network
  Wireless client isolation
  Captive portal
  IoT access considerations

## Slide 8: Security Threats to Wi-Fi Networks
War driving – a hacker searches for unprotected wireless networks by driving around with a laptop configured to receive and capture wireless data transmissions
War chalking – hackers draw symbols with chalk on the sidewalk or wall near a vulnerable AP to make it known to other hackers

## Slide 9: Security Threats to Wi-Fi Networks
Evil twin – a rogue AP planted in a network’s geological area to pose as an authorised AP
WPA attack – involves an interception of the network keys communicated between stations and APs
  Also called WPA cracking
WPS attack – involves cracking a PIN in order to access an APs settings
  The pin can be easily cracked through a brute force attack

## Slide 10: Wi-Fi Network Tools
Two types of software tools you should have:
  Spectrum analyser – a device that can assess the quality of the wireless signal
  Wireless analyser (Wi-Fi analyser) – software that can evaluate Wi-Fi network availability, optimise Wi-Fi signal settings, and help identify Wi-Fi security threats

## Slide 11: Wi-Fi Network Tools
List of capabilities common to wireless testing tools:
  Identify transmitting access points, stations, and channels
  Measure signal strength from an AP
  Indicate the effects of attenuation, signal loss, and noise
  Interpret signal strength information
  Ensure proper association and reassociation between APs
  Capture and interpret traffic
  Measure throughput and assess data transmission errors
  Analyse characteristics of each channel

## Slide 12: Avoid Pitfalls (1 of 2)
The following lists some wireless configuration pitfalls to avoid
No connection – when you cannot get the Wi-Fi client to connect to the AP:
  Wrong SSID
  Encryption protocol mismatch
  Incorrect passphrase
  Static channel utilisation
  Mismatched RF band
  Mismatched standards
  Long AP association time

## Slide 13: Avoid Pitfalls (2 of 2)
Slow connections – when dealing with slow Wi-Fi connections:
  Insufficient wireless coverage
  RF attenuation/signal loss
  Interference
  Channel overlap
  Wireless standard specifications
  Simultaneous wired and wireless connections
  Problems with firmware updates
  Incorrect antenna type
  Mismatched antenna polarisation
  Client saturation or overcapacity
  Client disassociation issues