## Slide 1: Wide Area Network (WAN) Essentials

## Slide 2: WAN Essentials
A WAN traverses a significant distance and usually supports very high data throughput
Type of WAN needed depends upon the following factors:
  Traffic load, budget, geographic breadth, and commercially available technology

## Slide 3: WAN Essentials
WAN and LAN differences include the following:
  LANs connect nodes; WANs connect networks spread over wide geographic area
  Differ at Layers 1 and 2 access methods, topologies, media
  Both LANs and WANs use the same protocols from Layer 3 and higher
  LANs are typically privately owned
  WANs are typically owned and operated by telcos, also known as NSPs (network service providers)
    Examples include AT&T, Verizon, Spectrum, and Comcast

## Slide 4: Entry Point Equipment (1 of 3)
If you have DSL or cable Internet service, you cannot your home router to a modem
  A modem is a demodulation device that converts digital and analog signals
Data Terminal Equipment (DTE) is the customer’s endpoint device on the WAN
  Communicates on the LAN and is usually owned by the customer

## Slide 5: Entry Point Equipment (1 of 3)
Data Communications Equipment (DCE) is the carrier’s endpoint device for the WAN
  Communicates on the WAN and is usually owned by the ISP
Equipment located on the customer’s premises is called CPE (customer premises equipment)
Demarc (demarcation point) is the point where the carrier’s responsibility ends, and the customer’s responsibility begins

## Slide 6: Entry Point Equipment (2 of 3)

## Slide 7: Entry Point Equipment (3 of 3)
The following are devices commonly found near the demarc:
  NIU (network interface unit) – connects the ISP’s local loop to the customer’s network
  Line driver – essentially a repeater that can boost the signal across greater distances
  CSU/DSU (channel service unit/data service unit) – serves as the endpoint for a dedicated connection between an ISP and a customer

## Slide 8: Routing Protocols (1 of 3)
A router joins two or more networks and passes packets from one network to another
Routers can do the following:
  Connect dissimilar networks (LANs and WANs)
  Interpret Layer 3 and often Layer 4 addressing
  Determine the best path for data to follow from point A to point B
  Reroute traffic if the path of first choice is down but another path is available

## Slide 9: Routing Protocols (1 of 3)
Routers may perform any of the following optional functions:
  Filter broadcast transmissions
  Prevent certain types of traffic from getting to a network
  Support simultaneous local and remote connectivity
  Provide high network fault tolerance through redundant components
  Monitor network traffic and report statistics
  Diagnose internal or other connectivity problems and trigger alarms

## Slide 10: Routing Protocols (2 of 3)
Router categories:
  Core routers, also called interior routers, direct data between networks within the same autonomous system (AS)
  Edge routers, or border routers, connect an autonomous system with an outside network
  Exterior routers refers to any router outside the organisation’s AS
    Direct data between autonomous systems

## Slide 11: Routing Protocols (3 of 3)

## Slide 12: Routing Tables (1 of 2)
A routing table is a database that holds information about where hosts are located and the most efficient way to reach them
  Routers rely on them to identify which router is the next hop to reach a particular destination host
Routing tables contain IP addresses and network masks that identify a network that a host or another router belongs to

## Slide 13: Routing Tables (2 of 2)

## Slide 14: Routing Path Types
Routing paths are determined in one of two ways
Static routing – A network administrators configures a routing table to direct messages along specific paths
  Example - a static route between a small business and its ISP
Dynamic routing – A router automatically calculates the best path between two networks and maintains this information in a routing table
  The router can detect problems with failed or congested routes and reroute messages through a different path

## Slide 15: route
The route utility allows you to view a host’s routing table
The route command can also be used to add or delete static routes
The following are some variations of the route command for different operating systems:
  On a Linux or UNIX system, use the command route
  On a Windows-based system, use the command route print
  On a Cisco IOS, use the command show ip route

## Slide 16: Routing Metrics
Routing metrics are properties of a route used by routers to determine the best path to a destination:
  Hop count
  Theoretical bandwidth and actual throughput
  Delay, or latency, on a potential path
  Load, or the traffic or processing burden
  MTU (maximum transmission unit), or the largest IP packet size in bytes allowable without fragmentation
  Routing cost, or a value assigned to a particular route
  Reliability of a potential path
  Topology of a network

## Slide 17: Routing Protocols to Determine Best Paths
Routing protocols are used by routers to communicate with each other to determine the best path
Routers rate the reliability and priority of a routing protocol’s data based on these criteria:
  AD (administrative distance) – a number indicating the protocol’s reliability
  Convergence time – the time it takes to recognise a best path in the event of a change or network outage
  Overhead – the burden placed on the underlying network to support the protocol

## Slide 18: Interior and Exterior Gateway Protocols (1 of 5)
IGPs (interior gateway protocols) are routing protocols used by core routers and edge routers within autonomous systems and are often grouped according to the algorithms they use to calculate best paths:
  Distance-vector routing protocols calculate path on the basis of the distance to that destination
  Link-state routing protocols enables routers to communicate beyond neighboring routers in order to independently map the network and determine the best path

## Slide 19: Interior and Exterior Gateway Protocols (1 of 5)
EGPs (exterior gateway protocols) are used by edge routers and exterior routers to distribute data outside of autonomous systems
  The only EGP currently in use is BGP

## Slide 20: Interior and Exterior Gateway Protocols (3 of 5)
OSPF (Open Shortest Path First) is an IGP, and a link-state protocol used on interior or border routers
  Characteristics include the following:
    Supports large networks - imposes no hop limits (unlike RIP)
    Complex algorithm – calculates a more efficient best path
    Shared data – maintains a database of other routers’ links
    Low overhead, fast convergence – demands more memory and CPU power for calculations, but keeps network bandwidth to a minimum and provides a very fast convergence time
    Stability – uses algorithms that prevent routing loops
    Multi-vendor routers – supported by all modern routers

## Slide 21: Interior and Exterior Gateway Protocols (4 of 5)
IS-IS (Intermediate System to Intermediate System) is an IGP and link-state routing protocol
  It uses a best-path algorithm similar to OSPF’s
  It is designed for use on core routers only (unlike OSPF)

## Slide 22: Interior and Exterior Gateway Protocols (4 of 5)
EIGRP (Enhanced Interior Gateway Routing Protocol) is an advanced distance-vector protocol that combines some of the features of a link-state protocol
  It is often referred to as a hybrid protocol
  Offers fast convergence time and low network overhead
  It is easier to configure and less CPU-intensive than OSPF
  Supports multiple protocols and limits unnecessary network traffic between routers
  EIGRP was originally proprietary to Cisco routers

## Slide 23: Interior and Exterior Gateway Protocols (5 of 5)
BGP (Border Gateway Protocol) is the only current EGP and is known as the “protocol of the Internet”
  BGP spans multiple autonomous systems
  Special characteristics of BGP include the following:
    Path-vector routing protocol
    Efficient
    Customisable
  BGP is the most complex of the routing protocols mentioned in this module

## Slide 24: Routing Redundancy
Large networks should have multiple ISP connections with each using geographically separate hardware and network media
Two redundancy techniques include the following:
  Active-active redundancy – all redundant resources are active at all times, and work is distributed among them
  Active-passive redundancy – only one or a few redundant resources are active at any time with the backup devices on standby

## Slide 25: Routing Redundancy
FHRP (First Hop Redundancy Protocol) can be used to provide a VIP (virtual IP) address as the default gateway
  VRRP (Virtual Router Redundancy Protocol)
  HSRP (Hot Standby Routing Protocol)
  GLBP (Gateway Load Balancing Protocol)