## Slide 1: Wide Area Network Connectivity

## Slide 2: WAN Connectivity
WAN connectivity options include the following:
  Broadband – cables and bandwidth are shared between multiple customers
    The ISP makes a “best effort” attempt to provide up to advertised bandwidth
    Bandwidth is asymmetrical (asynchronous) which means download speeds are faster than upload speeds
  DIA (dedicated internet access) – bandwidth is dedicated to a single customer
    Bandwidth is symmetrical (synchronous) which means download and upload speeds are about the same
    This is important for businesses that back up large amounts of data online

## Slide 3: DSL (Digital Subscriber Line) (1 of 2)
DSL (digital subscriber line) is a WAN connection method that operates over the PSTN (public switched telephone network)
DSL supports multiple data and voice channels over a single line
  It requires repeaters for longer distances
  The distance between the customer and CO affect actual throughput
DSL uses advanced data modulation techniques
A DSL connection might use a modulation technique based on amplitude or phase modulation to alter the waves at higher frequencies to carry data

## Slide 4: DSL (Digital Subscriber Line) (2 of 2)
The types of DSL vary according to their throughput rates, data modulation techniques, capacity, and distance limitations
  xDSL refers to all DSL varieties and the x is replaced by the variety’s name

## Slide 5: DSL (Digital Subscriber Line) (2 of 2)
Better-known DSL varieties:
  ADSL (asymmetric DSL) – faster download speeds than upload speeds
    Most common form of DSL
    Best use of ADSL is video conferencing and web surfing
  VDSL (very high bit rate DSL or variable DSL) – faster than ADSL and is also asymmetric
  SDSL (symmetric DSL) – has equal download and upload speeds maxing out around 2 Mbps
    Best use of SDSL is uploading and downloading significant data amounts

## Slide 6: Cable Broadband (1 of 3)
Cable broadband (also called cable Internet or cable modem access) is based on coaxial cable wiring used for TV signals
Cable broadband was standardised by an international cooperative effort
  It yielded a suite of specifications called DOCSIS (Data Over Cable Service Interface Specifications)

## Slide 7: Cable Broadband (1 of 3)
Service is typically offered at asymmetric speeds
  Such as up to 70 Mbps download and 7 Mbps upload
The newest DOCIS standard is 4.0 and allows for symmetric multi-gigabit speeds up to 10 Gbps downstream and 6 Gbps upstream
HFC (hybrid fibre coaxial) networks use fibre-optic cabling to connect the cable company’s distribution center to distribution hubs and then to optical nodes near customers

## Slide 8: Cable Broadband (2 of 3)

## Slide 9: Cable Broadband (3 of 3)
A cable modem modulates and demodulates signals for transmission and reception via cable wiring
  They operate at the physical and data Link layers of the OSI model
A cable modem may connect to connectivity device such as a router or switch
It is possible to use a device that combines cable modem functionality with a SOHO router to share available bandwidth on an entire network
Cable broadband provides a dedicated and continuous connection
It does require many subscribers to share the same local line which raises concerns about security and actual throughput

## Slide 10: Fibre (1 of 2)
A growing trend in ISP offerings for WAN connection services is to offer the following:
  FTTN (fibre-to-the-node or fibre-to-the-neighbourhood)
  FTTC (fibre-to-the-curb)
  FTTB (fibre-to-the-building) or FTTH (fibre-to-the-home)
MONs (metropolitan optical networks) bring fibre to the customer

## Slide 11: Fibre (2 of 2)

## Slide 12: Leased Lines
Leased lines provide dedicated bandwidth on fibre optic connections
A dedicated line offers the following advantages:
  Dedicated bandwidth
  Symmetrical bandwidth
  SLA-backed guarantee
Ongoing monthly costs of a leased line vary greatly depending on many factors:
  Required bandwidth
  The distance to the ISP’s exchange or between the company’s own locations

## Slide 13: MPLS (Multiprotocol Label Switching) (1 of 2)
MPLS (multiprotocol label switching) enables multiple types of Layer 3 protocols to travel over any one of several connection-oriented Layer 2 protocols
MPLS can handle various types of payloads
It is often used by ISPs on their own networks for moving traffic from one customer site to another

## Slide 14: MPLS (Multiprotocol Label Switching) (1 of 2)
MPLS labels include information about where the router should forward the message next
  The labels may also include prioritisation information
The primary benefits of MPLS include the following:
  MPLS connections are highly scalable for business
  Customers can prioritise their own traffic across the WAN
  The ability to label traffic offers more reliability, predictability, and security

## Slide 15: MPLS (Multiprotocol Label Switching) (2 of 2)

## Slide 16: Cloud Connectivity Options

## Slide 17: Software-defined WAN (SD-WAN) (1 of 2)
SD-WAN (software-defined wide area network) relies on abstracted, centralised control of networking devices to manage network functions across a diverse infrastructure
SD-WAN offers the following benefits:
  Transport agnostic
  Active-active load balancing and automatic failover
  Intent-based management
  Zero-touch provisioning
  Reduced cost

## Slide 18: Software-defined WAN (SD-WAN) (2 of 2)